## Slide 1: SNAMP: Secure Namespace Mapping to Scale NDN Forwarding
Alex Afanasyev (University of California, Los Angeles)
Cheng Yi (Google)
Lan Wang (University of Memphis)
Beichuan Zhang (University of Arizona)
Lixia Zhang (University of California, Los Angeles)
18th IEEE Global Internet Symposium (GI 2015)
April 27, 2015

## Slide 2: NDN overview: basics
Two types of packets
  Interest packet
    name
    nonce
    optional selectors
  Data packet
    name
    content
    signature
Names defined by applications
  /net/ndnsim/www/index.html/...
Name
Selectors (opt)
Nonce
Interest packet
Name
Content
Signature
Data packet

## Slide 3: NDN overview
NDN separates
  objective of retrieving
  specifics of how to do it
Interest names exactly what to fetch
  matching (secured) Data is retrieved by the network
  from caches, in-network storage, or data producers
Interest
In-network storage
Caches
Data
Notes: Interests should uniquely identify the requested Data

## Slide 4: Problem
NDN forwards interest by data names
  over 200 million just 2nd-level DNS names
  number of all names applications would use are several orders of magnitude larger, if not infinite
  even with all hierarchical aggregation, still too many names
How to scale NDN forwarding tables?

## Slide 5: Solution
Secure Namespace Mapping (SNAMP)
  To cross transit network, names may need to get mapped to (a set of) another names
  Interests will carry additional names to guide forwarding process
Based on map-n-encap idea
  proposed many years back to scale IP routing
    globally routable and non-routable addresses
    DNS to map
    IP-IP encapsulation to forward packets
    S. Deering. “The Map & Encap Scheme for scalable IPv4 routing with portable site prefixes.” Presentation Xerox PARC, 1996.
    M. O’Dell. “8+8—An alternate addressing architecture for IPv6.” Internet draft (draft-odell-8+8-00), 1996.
    D. Farinacci. “Locator/ID separation protocol (LISP).” Internet draft (draft-farinacci-lisp-00), 2007.
    R. Atkinson, S. Bhatti, and S. Hailes. “ILNP: mobility, multi-homing, localized addressing and security through naming.” Telecommunication Systems, 42(3), 2009.
map / encapsulate
User Networks
Transit networks

## Slide 6: General Goals
Keep the forwarding (routing) table size under control
  what goes to the table will be determined by
    popularity of the data
    network operation practices
    tradeoffs between network functionality and cost
Avoid any changes for NDN apps semantics
  no changes to naming of the data units
  no changes to apps

## Slide 7: A Few Terms
FIB
  forwarding information base (~routing table)
DFZ
  default free zone (core transit network)
Namespace delegation
  owner of namespace endorses that interests for the data in the namespace can be satisfied if forwarded towards another namespace
    (/net/ndnsim) -> (/telia/latvia/terabits)
LINK object or just LINK
  collection of delegations with preferences from the same namespace
    (/net/ndnsim) -> (/telia/latvia/terabits 100; /ucla/cs 10)

## Slide 8: System Overview

## Slide 9: More Design Goals and Considerations
Do not require routers lookup mapping
Do not require changes to the application
  a local agent (local NFD?) or an application library performs lookup when needed
Invoke mechanism only when necessary
  A lot of communication is expected to be local and ad hoc

## Slide 10: Data Retrieval with SNAMP (1)

## Slide 11: Data Retrieval with SNAMP (2)

## Slide 12: Data Retrieval with SNAMP (3)

## Slide 13: Multiple Delegations in the LINK Object
Reasons
  Producer multihoming
  Replicated dataset
Impact on interest forwarding
  NDN network is supposed to forward interests towards “closest” data available
  End-hosts/consumer-networks don’t have knowledge which is “closer”
    can pick at random and learn over time
  DFZ routers have routing and data plane performance parameters
    informed choice

## Slide 14: Data Retrieval with SNAMP (summary)

## Slide 15: Discovery of the LINK Object
Pre-configured knowledge
Application-level exchange
  Real-time producer can “give” a new link to consumers, when changes occur
  LINK can be “sync”ed up
Discovery using infrastructure support
  NDNS (DNS for NDN, https://github.com/named-data/ndns)
Notes: ChronoChat and ChronoShare

## Slide 16: Simplified Picture of NDNS Lookup*
* Real NDNS lookup includes discovery of NS records and key records to verify validity of the data

## Slide 17: “Devils are in Details”

## Slide 18: “Evil” Details
Format of LINK and how it is included in the Interest
Modification of interest forwarding
  Impact on processing time/complexity
  Possible optimizations
Effects on caches
  Resiliency to content poisoning
  Cache effectiveness

## Slide 19: Format and Use of LINK Object

## Slide 20: Updated Interest Forwarding
If LINK not present
  apply standard NDN interest forwarding logic
  return NACK/no-route if interest cannot be forwarded
if LINK present
  (if router choses so) verify validity of the link
  if LINK includes name of the “own network”
    apply standard NDN interest forwarding logic
  Lookup LINK delegations in FIB, select “best”, and forward
Notes: 1/ the above did not include the case where interest needs to be forwarded to a router that a mobile registred with
2/ suggest you explain the basic concept: LINK carries Interest to the domain where true data name is reachable (can be a network or a node)

## Slide 21: Example of Interest Forwarding
/net/ndnsim
is registered with UCLA CS router
/ucla/cs/www
/ucla/cs/...
/net/ndnsim
default
FIB

## Slide 22: Example of Interest Forwarding
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/net/ndnsim/www/index.html
+
/net/ndnsim/www =>
- /ucla/cs, 1
- /telia/terabits, 1

## Slide 23: Example of Interest Forwarding
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/telia 100
/ucla 10
FIB
/net/ndnsim/www/index.html
+
/net/ndnsim/www =>
- /ucla/cs, 1
- /telia/terabits, 1

## Slide 24: Example of Interest Forwarding
/ucla/cs/www
/ucla/cs/...
/net/ndnsim
default
FIB
/net/ndnsim/www/index.html
+
/net/ndnsim/www =>
- /ucla/cs, 1
- /telia/terabits, 1
Own Network
/ucla/cs

## Slide 25: “Own Network” Concept
Routers need to know to which network(s) they belong
  configuration
  automatic discovery
Until interest reaches “own” network
  can be satisfied from cache based on name of the interest
  forwarded strictly using LINK, even if interest name is in the forwarding table
    need to allow /ucla/cs/alex/homepage to be hosted outside UCLA

## Slide 26: Processing Optimization
When LINK present and router makes forwarding decision based on non-default route
  decision can be recorded and upstream routers can just use it
“SelectedDelegation”

## Slide 27: Effects on Caches
Resiliency to content poisoning
  When data packets cached, it must be associated with LINK that used
  For interest to match cached item, both name and LINK must match
    Even when routers don’t very LINKs, malicious injected data does not effect legitimate users
Cache effectiveness
  “Normally” there is a single legitimate LINK
    No change to cache effectiveness

## Slide 28: Tradeoffs for the Updated Forwarding
Gains
  Routing table is under control
  Routers make conscious decisions on where to forward interest
Issues
  increased complexity per-interest processing
    multiple FIB lookups

## Slide 29: Thanks