## Slide 1: Similar Yet Different Protocol Design Choices in IS-IS and OSPF
Yu Zhang (Harbin Institute of Technology), Lan Wang (University of Memphis), Alex Afanasyev (Florida International University), Lixia Zhang (UCLA)
Asian Internet Engineering Conference (AINTEC 2017) November 21, 2017 Bangkok, Thailand

## Slide 2: Goals
Compare two similar yet different link-state (LS) routing protocols
  Intermediate System to Intermediate System (IS-IS)
  Open Shortest Path First (OSPF)
Inform design new link-state routing protocols for new network architectures
  How should one design a new link-state routing protocol from scratch?
Notes: each router uses Dijkstra’s shortest path computation algorithm to compute the best path(s) on a whole topology

## Slide 3: Ten questions on link-state routing design
How to uniquely identify a router?
How to organize and identify LS data?
How to format LS data in packets?
Which types of messages are in protocols?
How to establish adjacencies between neighbors?
How to sync data between neighboring routers over a point-to-point link?
How to establish adjacencies in a broadcast network?
How to sync data in a broadcast network?
How to abstract a graph from an LSDB (LS database)?
How to design a hierarchical routing scheme?
The main task of the protocol is to describe, discover, and disseminate the network topological information

## Slide 4: 1. How to uniquely identify a router?
RID=OSI NSAP address = Area ID+System ID
System ID = MAC addr or IP addr
RID=the highest/lowest IP address on its active logical (loopback) interfaces and physical interfaces
IS-IS
OSPF
Direct way: RIDs are directly assigned by a center or manually configured by an operator
Indirect way: each router independently derives its own RID from some of its own properties which may be obtained in some centralized ways, such as MAC addr
Where does the uniqueness come from?

## Slide 5: 2. How to organize and identify LS data?
LSU: LS PDU (LSP)
1-dimensional organization
ID: the advertising router RID
Content: all LS data advertised by the same router
Fragmentation if LSU size>MTU
LSU: LS Advertisements (LSA)
3-dimensional organization
ID: LS-TYPE, LS-ID, RID
  LS-ID is determined different for different LS-TYPE
Content: data identified by ID
IP fragment if LSU size>MTU
IS-IS
OSPF
IS-IS 1-dimension: simpler, but bigger update
OSPF 3-dimension: finer, but more overhead to describe LSDB
2-dimension: RID+X (X could be a type ID)
What is a LS Unit (LSU)? a minimal piece of LS data which can be individually sent and updated.

## Slide 6: 3. How to format LS data in packets?
OSPFv2
IS-IS
LS ID
Advertising Router
LS Age
Options
LS Type
LSA Sequence Number
LSA Checksum
Length
Static Format Content…
PDU Length
Remaining Lifetime
LSP ID
Sequence Number
Checksum
P/ATT/LSPDBOL/IS
Type/Length/ Values Fields
Necessary fields: RID, Sequence Number, Age/Lifetime
TLV is extensible; static field format is hardware-friendly
What field is put in an LSU and how ?

## Slide 7: 4. Which types of messages are in protocols?
IS-IS | OSPF | Function
Hello | Hello | For the adjacency establishment
CSNP | DB Desc | Describe the state of a router’s LSDB
Update | Update | Update message containing an LSU
PSNP(REQ) | Request | Request for LSUs from other routers
PSNP(ACK) | ACK | Acknowledge the receipt of LSUs
Necessary message types: Hello, Update
For the rest three, the design heavily depends on the synchronization method.
Request and ACK messages (also PSNPs) can be replaced by periodically sending DBDS (CSNP) messages and pushing Update messages.

## Slide 8: 5. How to establish adjacencies between neighbors?
The distinction between two protocols is on the timing of advertising adjacency.
In IS-IS, Adj=BFC; In OSPF, Adj=BFC+LSDB Sync
Advertising-after-synchronizing method: the adjacency establishment is separated from the synchronization as in IS-IS, but the advertisement is postponed until the initial synchronization is completed as in OSPF.
IS-IS
OSPF
Hello from A
Neighbor: -
Hello from B
Neighbor: A
Hello from A
Neighbor: B
LSDB
initial sync
Bidirectional Forwarding capability (BFC) detection by 3way handshaking

## Slide 9: 6. How to sync data over a point-to-point link?
IS-IS
OSPF
Two options for transmitting differences in the initial sync: push in IS-IS; pull in OSPF
One inspiration from IS-IS: sync by periodically sending CSNPs as implicit requests. Practical if the cost of representing LSDB is low.
CSNP
Update
PSNP(ACK)
initial sync
Update
ACK
DBDS
Request
Update
ACK
Update
PSNP(ACK)
or
Update
update
PSNP(ACK)
Update

## Slide 10: 7. How to establish adjacencies in a broadcast network?
Designated Router (DR)
IS-IS
Psuedo-node
OSPF
Mesh
How to make the network topology sparse?
The choice of DR election method depends on whether a DR is heavy-duty and maintains much information.
  Yes. In IS-IS, the election is preemptive: a new router with higher priority can take the status of DR from the old DR.
  No. In OSPF, the DR status is sticky: the DR will not be changed unless it crashes.
The sparsified topology is a star

## Slide 11: 8. How to sync data in a broadcast network?
(A)
(B)
How to make the sync relationship sparse?
As Fig. (B), all routers synchronize only with the DR as in a p2p link
OSPF
As in Fig. (A), routers broadcast updates directly to each other;
As in Fig. (B), only the DR periodically broadcasts CSNPs as implicit acknowledgments
IS-IS
The DR in IS-IS is like a ‘spokesman’ speaking for the pseudo-node and sending CSNPs on behalf of non-DR routers
the DR in OSPF is like a ‘leader’ leading the adjacency establishment and the LSDB sync among non-DR routers

## Slide 12: 9. How to abstract a graph from an LSDB?
R3
R4
R5
N2
N3
6
7
1
N1
R1
R2
R3
R4
R5
1
6
7
N3
N2
P1
R1
R2
N1
R3
R4
R5
2
3
4
5
6
N3
N1
R1
R2
1
N2
OSPF
IS-IS
Physical
Separated vs. Integrated
We prefer “separated”, a benefit is that a change on the reachability will not necessarily trigger an SPF recalculation.
a broadcast network with two p-to-p routers
a host with 2 p-to-p links
a broadcast network with only one router
a broadcast network with three routers
adjacency and reachability are separated
adjacency and reachability are integrated

## Slide 13: 10. How to design a hierarchical routing scheme?
L2
L2
L2
L1/2
L1/2
L1
L1
L1
L1
ABR
ABR
IS-IS
OSPF
A single backbone area as a center of star topology among areas
In terms of the knowledge of LS data, boundaries cross routers in both protocols.
An alternative design is to draw boundaries across links by making each router maintain only one LSDB for its own area.

## Slide 14: A complement to the reason for diverse protocol designs
It is Design Style
The design choices of IS-IS largely reflects more considerations on logical abstraction
The design choices of OSPF reflect more pragmatic consideration

## Slide 15: Conclusions
IS-IS and OSPF protocols fulfill the same network routing functions through different designs.
We believe that routing protocol designs, and network protocol designs in general, are still in the stage of being a design art.
We believe that the future Internet architecture should be designed to make it easier to solve the above common protocol design issues, e.g., naming and efficient information dissemination

## Slide 16: Thanks!